## Slide 1
Newspaper Towers
by Robert Chen
Engineering/Construction/Challenge
Elementary or High School
Spring 2013
Notes: You can change the subtitle to whatever is appropriate.

## Slide 2: Challenge and Teaching Points
Challenge
Build the tallest free-standing structure out of newspaper possible.
Can be taped to surface at its base only.
Teaching Points
Triangles are strong
5-step design process
Trial and error construction
Teamwork

## Slide 3: Agenda
Intro (10min)
  Introduce challenge
  Talk about why triangles are strong
  Shapes demo
  Pleated paper demo
  Examples of triangles
  5-step engineering design process
  Give materials only after they sketch a design

## Slide 4: Agenda (con’t)
Build (40min)
  4-10 newspapers, your choice
  Start with 1 foot of tape
  I want tape to be limited to hopefully foster creativity
Recap (5min)
  Point out where they used triangles effectively
  Give them positive feedback about what they did to create strong structures

## Slide 5: Why are triangles strong?
Fewer degrees of freedom than many other shapes
Given sides of constant length, you can’t change angles of a triangle
Force on a triangle goes into the material of the sides and the strength of the pivot in the joints
K = 2J – 3
M = number of members (beams)
J = number of joints
R = 3, number of sides of triangle
K = M, stable
K > M, unstable
K < M, indeterminate

## Slide 6: Shapes demo
Point is to show that you can deform a square, but not triangles.
We will make these with cardboard and the fasteners later. Bring them to your site.

## Slide 7: Pleated paper demo
Point is to show that force can be distributed over many triangles to be fairly strong.

## Slide 8: Examples of triangles

## Slide 9: 5-step engineering design process
Ask what makes a good tower
Imagine possible designs
Plan tower on paper
Create out of newspaper
Improve it

## Slide 10
A tower made with no tape, just 9 newspapers

## Slide 11: Fastening without tape
Front
Back

## Slide 12: Every site grab…
Cardboard
6 newspapers
11 fasteners
Scissors
Foot of tape